## Slide 1: How does Deepspeed ZeRO perform distributed training to train LLMs

## Slide 2: Contents
Background
Opportunities and Challenges in distributed training
  w.r.t. communication, network, parallelism search
Distributed training works
  w.r.t. communication, throughput, ease of use, scalability and resilience
Deepspeed ZeRO trilogy
  ZeRO, ZeRO-Offload, ZeRO-Infinity

## Slide 3: Why we need distributed training ?
Achieve higher utilization of GPU
Price scissorsbetween Parameters Size and Memory Capacity

## Slide 4: Opportunities and Challenges in distributed training
Parallelism Strategy
Network and Communication Optimization
Other Optimizations

## Slide 5: Background - Collective Communication
all-reduce
reduce-scatter
all-gather

## Slide 6: Background - Communication Bandwidth
Inter-node (100 ~ 800 Gbps)
  Ethernet
  InfiniBand
Intra-node
  CPU – GPU : 10
  GPU – GPU : 100
    PCIe (a100:64GB/s h100:128GB/s)
    NVLink (600 ~ 900 GB/s)
  CPU – NVMe SSD : 1

## Slide 7: Background - Memory Footprint
Memory Footprint
Mixed Precision Training
Adam Optimizer
Residual States: FP16 Activations and others
Model States: FP32 weights, FP32 momentum, FP32 variance, FP16 weights
FP16 gradients, (FP32 gradients)

## Slide 8: Distributed training methodology
Pipeline Model Parallelism
Tensor Model Parallelism
Data Parallelism
ZeRO Data Parallelism

## Slide 9: Data Parallelism
Procedure
Forward locally
Backward locally
Gradient All-reduce globally
Update weights locally
Cons
Every rank holds a whole Model Shard thus has worst memory efficiency.
In large scale GPU cluster, little batch size lead to low utilization & high communication cost.
Pros
Each model takes a different micro-batch.
Relatively low communication cost than model parallelism.
Ease of use.

## Slide 10: Pipeline Model Parallelism
Procedure
Forward locally, send output to the next rank.
If there are enough micro-batches, keep perform step 1.
Else go into Bubble until backward start.
Backward locally, send output to previous rank.
Keep doing until the iteration ends(pipeline flush)
Cons
Need large micro batch size to hide pipeline bubble and flush.
Large micro batch thus causing high activation memory footprint & convergence issue.
It’s of difficulty to divide balanced pipeline workload.
Pros
Each model takes a different micro-batch, which a part of the input batch.
Communication cost is relatively low. (one point-to-point communication).
Bubble fraction =

## Slide 11: Pipeline Model Parallelism
Decrease In-flight memory footprint
Decrease bubble fraction
Bubble fraction =

## Slide 12: Tensor Model Parallelism
Procedure
Divide weight vertically into A_1 & A_2
Multiply input X with A_1, A_2 in rank_0, rank_1 respectively
Perform GeLU respectively
All reduce
Peform Dropout respectively
Cons
Higher communication cost. Per MLP/attention a all-reduce operation.
Need to store multiple copy of input
Need to modify source code. (But they claim that it’s easy).
High degree of TP decrease GPU utilization
Pros
Effective in Transformer-based models in small scale of GPU cluster.

## Slide 13: PTD(3D) Parallelism
for pipe in pipeline_parallelism
for tensor in tensor_parallelism
for mb in data_parallelism
perform dp(pipe, tensor, mb)
end
perform tp(pipe, tensor)
end
perform pp(pipe)
end

## Slide 14: Deepspeed-ZeRO / FSDP
Pros
Have same or better effectiveness than PP / TP.
Be able to scale out to 1000B using only ZeRO data parallelism.
Less communication cost than TP.
Cons
Like Data parallelism. Low GPU utilization.

## Slide 15: Deepspeed-ZeRO-1
Fp32 optimizer state
Fp16 weight
Fp16 gradient
ZeRO-Stage | Memory consumed | Communication Volume
ZeRO-1 |  | 
ZeRO-2 |  | 
ZeRO-3 |  | 
ZeRO-Stage | Memory consumed | Communication Volume
ZeRO-1 |  | 
ZeRO-2 |  | 
ZeRO-3 |  | 
All Gather
All Reduce

## Slide 16: Deepspeed-ZeRO-2
Fp32 optimizer state
Fp16 weight
Fp16 gradient
ZeRO-Stage | Memory consumed | Communication Volume
ZeRO-1 |  | 
ZeRO-2 |  | 
ZeRO-3 |  | 
ZeRO-Stage | Memory consumed | Communication Volume
ZeRO-1 |  | 
ZeRO-2 |  | 
ZeRO-3 |  | 
All Gather
Reduce-Scatter

## Slide 17: Deepspeed-ZeRO-3
Fp32 optimizer state
Fp16 weight
Fp16 gradient
ZeRO-Stage | Memory consumed | Communication Volume
ZeRO-1 |  | 
ZeRO-2 |  | 
ZeRO-3 |  | 
ZeRO-Stage | Memory consumed | Communication Volume
ZeRO-1 |  | 
ZeRO-2 |  | 
ZeRO-3 |  | 
All Gather
Reduce-Scatter

## Slide 18: Deepspeed-ZeRO-3

## Slide 19: Deepspeed-ZeRO-Offload

## Slide 20: Deepspeed-ZeRO-Offload

## Slide 21: Deepspeed-ZeRO-Offload

## Slide 22: Deepspeed-ZeRO-Infinity
Memory Defragmentation
Overlap Centric Design
Operator Break down

## Slide 23: Deepspeed-ZeRO-Infinity

## Slide 24
Thanks For Listening ! ! !